memo

variables

equations

{dE} over {dt}= ( frac {N_{0}V_{core}E_{fiss} } {τ} ) func e^{ ( {α} wideslash {τ} ) t} newline V_core= frac {4} {3}πr^{3} newline P_{ core }( t )= frac {γE (t) } {V_{core} (t) } newline d_{core}= sqrt{ frac {λ_{core fiss}λ_{core trans}} {3 (-α+ν-1) } } newline ( R_C / d_core ) cot( R_C / d_core )+( 3d_core / 2λ_{core trans} ) ( R_C / d_core )-1=0 newline τ= frac {λ_{core fiss}} {v_neut} newline λ_{core fiss} = {1} over {σ_f n} newline λ_{core trans}= frac {1} {σ_{t}n} newline σ_{ t }=σ_{ f }+σ_{ el } newline

Ncore: number density of neutron.
= Numbers/Vol

N0, U235: Nneutron=143, 9.48*10^20 [atoms / cm3]
→ (143*9.48*10^20) [neutrons / cm3] = (143*9.48*10^20)*10^6 [neutrons / m3]
https://www.nuclear-power.com/nuclear-power/reactor-physics/nuclear-engineering-fundamentals/neutron-nuclear-reactions/atomic-number-density/
https://en.wikipedia.org/wiki/Uranium-235

n: number density of nuclear = (mass number)/(4/3*pi*R^3)
R= 1.25 [fm] = 1.25*10^(-15) [m]
mass number, U235= 235
n= 235/(4/3*pi*(1.25*10^(-15))^3)

https://en.wikipedia.org/wiki/Nuclear_density

molecular weight of U235 = 235.04393
https://pubchem.ncbi.nlm.nih.gov/compound/Uranium-235

sigmaF: fission cross-section of fissile material.
U235, 1 [MeV]: 1.199 [Barns] = (1.199*10^(-28)) [m2]

sigmaEl: elastic-scattering cross section of fissile material.
U235, 1 [MeV]: 3.650 [Barns] = (3.650*10^(-28)) [m2]

vNeutron: average speed of neutron
emitted by fission: 1.4x10^9 [cm/sec] = 1.4x10^7 [m/sec]

nu: number of neutrons emitted per fission
2.43 [neutrons]
https://www.nuclear-power.com/nuclear-power-plant/nuclear-fuel/uranium/uranium-235/uranium-235-fission/

https://en.wikipedia.org/wiki/Nuclear_chain_reaction

dCore: critical radius

https://nuclearweaponarchive.org/Nwfaq/Nfaq4-1.html