memo

Critical mass is converged into single piece

Fission chain reaction begins.

Release of huge amount of energy = Explosion

Neutron is captured by atom.
Atom breaks apart into multiple pieces.

Multiple new neutrons are emitted.

Energy release.

Cause other fissions
 = chain reaction

Single fission reaction.

parameters / constants

N_0: initial neutron number density dotsaxis [1] newline E_fiss: energy released by single fission reaction dotsaxis [2] newline γ: pressure parameter dotsaxis [3] newline ν: secondary neutrons dotsaxis [4] newline σ_f: fission cross section of fissile material dotsaxis [5] newline σ_el: elastic-scattering cross section dotsaxis [6] newline n_0: initial nuclear number density dotsaxis [7] newline r_0: initial core radius dotsaxis [8] newline v_neut: average neutron speed dotsaxis [9]

variables

E: cumulative nergy released dotsaxis [1] newline V_core: core volume dotsaxis [2] newline v_core: speed of core expansion newline τ: average time neutron will travel before causing fission dotsaxis [3] newline α: criticality parameter dotsaxis [4] newline r: radius of core dotsaxis [5] newline p_core: pressure of core dotsaxis [6] newline d_core: critical radius dotsaxis [7] newline λ_{core fiss}: mean free path between fissions dotsaxis [8] newline λ_{core trans}: transport mean free path for neutrons dotsaxis [9] newline σ_t: transport cross section dotsaxis [10] newline n: nuclear number density dotsaxis [11] newline n_nuke: number of nucleous dotsaxis [12] newline K_core: kinetic energy of core dotsaxis [ 13 ]

equations

{dE} over {dt}= ( frac {N_{0}V_{core}E_{fiss} } {τ} ) func e^{ ( {α} wideslash {τ} ) t} dotsaxis [1] newline V_core= frac {4} {3}πr^{3} dotsaxis [2] newline frac {dv_core} {dt}= frac {4πr^2 γE} {V_core m_core} dotsaxis [3] newline frac {dK_core} {dt}= p frac {dV} {dt} dotsaxis [4] newline p_{ core }( t )= frac {γE (t) } {V_{core} (t) } dotsaxis [5] newline d_{core}= sqrt{ frac {λ_{core fiss}λ_{core trans}} {3 (-α+ν-1) } } dotsaxis [6] newline ( r / d_core ) cot( r / d_core )+( 3d_core / 2λ_{core trans} ) ( r / d_core )-1=0 dotsaxis [7] newline τ= frac {λ_{core fiss}} {v_neut} dotsaxis [8] newline λ_{core fiss} = {1} over {σ_f n} dotsaxis [9] newline λ_{core trans}= frac {1} {σ_{t}n} dotsaxis [10] newline σ_{ t }=σ_{ f }+σ_{ el } dotsaxis [11] newline n= n_nuke / V_core dotsaxis [12] newline n_nuke= n_0 * frac {4} {3} π r_0^3 dotsaxis [13]

Ncore: number density of neutron.
= Numbers/Vol

N0, U235: Nneutron=143, 9.48*10^20 [atoms / cm3]
→ (143*9.48*10^20) [neutrons / cm3] = (143*9.48*10^20)*10^6 [neutrons / m3]
https://www.nuclear-power.com/nuclear-power/reactor-physics/nuclear-engineering-fundamentals/neutron-nuclear-reactions/atomic-number-density/
https://en.wikipedia.org/wiki/Uranium-235

n: number density of nuclear = (mass number)/(4/3*pi*R^3)
R= 1.25 [fm] = 1.25*10^(-15) [m]
mass number, U235= 235
n= 235/(4/3*pi*(1.25*10^(-15))^3)

https://en.wikipedia.org/wiki/Nuclear_density

molecular weight of U235 = 235.04393
https://pubchem.ncbi.nlm.nih.gov/compound/Uranium-235

sigmaF: fission cross-section of fissile material.
U235, 1 [MeV]: 1.199 [Barns] = (1.199*10^(-28)) [m2]

sigmaEl: elastic-scattering cross section of fissile material.
U235, 1 [MeV]: 3.650 [Barns] = (3.650*10^(-28)) [m2]

vNeutron: average speed of neutron
emitted by fission: 1.4x10^9 [cm/sec] = 1.4x10^7 [m/sec]

nu: number of neutrons emitted per fission
2.43 [neutrons]
https://www.nuclear-power.com/nuclear-power-plant/nuclear-fuel/uranium/uranium-235/uranium-235-fission/

https://en.wikipedia.org/wiki/Nuclear_chain_reaction

dCore: critical radius

https://nuclearweaponarchive.org/Nwfaq/Nfaq4-1.html

Memo:
計算式のmmlファイルへの保存：計算式ボックスを左クリックで選択　→　右クリック　→　「名前を付けてコピーを保存」　→　「MathML 2.0」を選択